## Slide 1: Using the pipets
(properly)

## Slide 2
This is a P1000
This is the range of volume it covers.
Do not go above the highest #, or below the lowest #.
This is the 1000s place.
This is the 100s place.
This is the 10s place.
This is the 1s place (the gradiation marks).
This pipet goes from 100-1000 uL with an accuracy of 1 uL
Do not just leave this at the highest or lowest value. Pipets function by a spring. Compressing or stretching the spring for too long, or outside of it’s bounds, damage the spring and de-calibrate the pipet.
This pipet currently reads 639 uL

## Slide 3
This is a P200
This is the range of volume it covers.
Do not go above the highest #, or below the lowest #.
This is the 100s place.
This is the 10s place.
This is the 1s place.
This is the 10ths place.
This pipet goes from 20.0-200.0 uL with an accuracy of 0.1 uL
Do not just leave this at the highest or lowest value. Pipets function by a spring. Compressing or stretching the spring for too long, or outside of it’s bounds, damage the spring and de-calibrate the pipet.
This pipet currently reads 138.8 uL

## Slide 4
This is a P20
This is the range of volume it covers.
Do not go above the highest #, or below the lowest #.
This is the 10s place.
This is the 1s place.
This is the 10ths place.
This is the 100ths place.
This pipet goes from 2.00-20.00 uL with an accuracy of 0.01 uL
Do not just leave this at the highest or lowest value. Pipets function by a spring. Compressing or stretching the spring for too long, or outside of it’s bounds, damage the spring and de-calibrate the pipet.
This pipet currently reads 4.00 uL

## Slide 5
This is a P2.5
This is the range of volume it covers.
Do not go above the highest #, or below the lowest #.
This is the 1s place.
This is the 10ths place.
This is the 100ths place.
This is the 1000ths place.
This pipet goes from 0.1-2.5 uL with an accuracy of 0.001 uL
Do not just leave this at the highest or lowest value. Pipets function by a spring. Compressing or stretching the spring for too long, or outside of it’s bounds, damage the spring and de-calibrate the pipet.
This pipet currently reads 1.668 uL